## Slide 1
SOFTWARE ARCHITECTURE DESIGN
Expansion Module for
Fuel-Cell Systems
Four configurable analogue inputs, configuration that survives a power interruption, and a CAN interface to the fuel-cell system controller.
4
analogue inputs
CH0–CH3, wired straight to the
microcontroller's ADC
3+1
channel types
temperature, current, voltage
— or disabled
1
external interface
the CAN bus is the module's
entire external API
0
operating systems
a cyclic executive, chosen
deliberately over an RTOS
REQUIREMENTS · SYSTEM CONTEXT · LAYERED ARCHITECTURE · DATA PATH · CONFIGURATION · EXECUTION · TEST · CONCLUSION
Notes: [0:40]
Thanks. The task was to design a software architecture for an expansion module for fuel-cell systems. The module has four analogue inputs wired directly to the microcontroller's ADC, and a CAN interface back to the fuel-cell system controller. Each input can be a temperature, current or voltage measurement — and that setting has to survive a power interruption.
Four numbers frame the design: four channels, three sensor types plus disabled, one external interface, and no operating system. I'll spend most of the time on the architecture, and on the two hard parts — persistence and determinism.

## Slide 2
01 · REQUIREMENTS
What the module must do, and what I chose
Separating the requirements that come from the brief from the design decisions I made to satisfy them.
FUNCTIONAL — FROM THE BRIEF
1
Acquire
Sample CH0–CH3 through the microcontroller's own ADC inputs.
2
Configure
Set each channel to temperature, current, voltage or disabled over CAN.
3
Persist
Restore the last committed configuration after a power interruption.
4
Publish
Expose the current value and per-channel status through the predefined CAN protocol.
QUALITY — HOW WELL IT MUST DO IT
1
Deterministic
Bounded, periodic execution. No unbounded wait and no sleep in the acquisition path.
2
Robust
Invalid commands are rejected and the last committed configuration stays in force.
3
Diagnosable
Channel validity, module health, CAN state and reset reason are all observable.
4
Testable
Services depend on interfaces, so the ADC, CAN, NVM and timer drivers can all be mocked on a host.
KEY DESIGN DECISIONS — MINE
1
Bare-metal cyclic executive
Four channels and five short periodic jobs do not justify RTOS scheduling.
2
Interrupts stay short
The timer ISR only counts; the CAN Rx ISR only queues a frame. All work runs in the main context.
3
Fixed conversion profiles
Sensor type selects compile-time conversion logic. No field calibration is exposed.
4
Two-copy committed record
CRC, sequence number and commit marker make an interrupted NVM write survivable.
Notes: [1:05]
Before drawing any boxes, I separated what the brief gives me from what I decided.
On the left, the four functional requirements straight out of the task: acquire, configure, persist, publish. In the middle, the qualities that aren't written down but decide whether the design is any good — deterministic timing, robustness to bad input, diagnosability, and testability.
On the right, my decisions. A bare-metal cyclic executive rather than an RTOS: four channels and five short periodic jobs don't justify the scheduling complexity or the analysis burden. Interrupts stay short — the timer interrupt only counts, and the CAN receive interrupt only queues a frame. Conversion profiles are fixed at compile time, so there's no field calibration to get wrong. And the configuration is a two-copy record with a CRC, a sequence number and a commit marker.
Every one of those is reversible, and I'm happy to argue any of them.

## Slide 3
02 · SYSTEM CONTEXT
One microcontroller, four inputs, one bus
The physical boundary of the module, and where the firmware sits inside it.
4 ANALOGUE
INPUTS
CH0 – CH3, each set to
· temperature
· current
· voltage
· disabled
FUEL-CELL
SYSTEM
CONTROLLER
EXPANSION MODULE
SIGNAL
CONDITIONING
· divider / shunt amp
· RTD front end
· anti-alias filter
· over-voltage clamp
· scaled to 0 – 3.3 V *
MICROCONTROLLER
ADC
4 channels
scan mode
12-bit *
FLASH /
EEPROM
configuration
record (NVM)
APPLICATION
FIRMWARE
· Measurement Manager
· Sensor Converter
· Configuration Manager
· CAN Protocol Manager
· NVM Manager
· Diagnostics Manager
· Cyclic Scheduler
· State Machine
CAN
controller
mailboxes
filters
error state
TIMER +
WDG
1 ms tick *
reset on stall
CAN
TRANSCEIVER
differential
physical layer
CAN bus
* Working assumptions, not requirements — the real figures come from the chosen microcontroller and the system specification.
Where the boundary sits
The module owns the conditioning, the microcontroller and the transceiver. Sensor selection and bus topology sit outside it.
Why the ADC is internal
The brief wires each input straight to an MCU ADC channel. The conditioning shown is passive scaling and protection — no external converter to drive.
One processor, no operating system
All six services, the scheduler and the HAL run on this single microcontroller. There is no second processor.
Read it left to right — analogue in, digital out. The CAN bus is the only path off the module, which makes the CAN Protocol Manager the module's entire external API.
Notes: [1:10]
This is the physical boundary.
On the left, the four analogue inputs. Then passive signal conditioning — dividers, a shunt amplifier, an RTD front end, filtering and over-voltage protection — scaling everything into the ADC's range. The brief wires the inputs straight to the microcontroller's ADC, so there's no external converter to drive or synchronise.
Inside the microcontroller: the ADC, the flash holding the configuration record, the CAN controller, a timer and watchdog, and the application firmware — six services and a scheduler, all on this one part. No second processor, no operating system. Then the transceiver, and the bus out to the fuel-cell controller.
Read it left to right: analogue in, digital out. The architectural point is that the CAN bus is the only path off the module, which makes the CAN Protocol Manager the module's entire external API.
The starred figures are working assumptions I'd confirm with the system owner, not requirements.

## Slide 4
03 · SOFTWARE ARCHITECTURE
Three layers, one direction of dependency
Arrows follow a measurement, left to right. Calls run the opposite way, right to left, and never back.
OUTSIDE THE SOFTWARE
HAL / DRIVERS
APPLICATION SERVICES
EXECUTION
4 analogue inputs
CH0 – CH3
Temperature · Current
Voltage · Disabled
Fuel-cell controller
sends configuration,
receives values and status
over the predefined CAN protocol
ADC HAL
start · read · status
CAN HAL
rx · tx · error state
NVM HAL
read · write · verify
Timer + WDG HAL
tick · reset · service
Measurement Manager
owns samples, values,
timestamps and channel status
Sensor Converter
dispatches the fixed conversion
for each SensorType
Configuration Manager
validates and owns the
four channel modes
CAN Protocol Manager
decodes commands, packs
values and status
NVM Manager
two-copy record, CRC,
sequence and commit marker
Diagnostics Manager
collects faults, counters
and the reset reason
Cyclic Scheduler
releases the periodic jobs
in a fixed order, every pass
State Machine
INIT
RUN
DEGRADED
BUS-OFF RECOVERY
The left column is context, not a layer — the inputs and the controller are actors outside the module's software.
Three layers, no more
Hardware access, application services, execution control. A fourth layer would buy nothing at this size.
One owner per piece of state
The configuration lives in the Configuration Manager, measurements in the Measurement Manager. No service writes another's data.
Swap the bottom layer out
Replace the four HAL modules with fakes and the whole upper stack runs, and is tested, on a host PC.
Notes: [1:25]
This is the core of the answer. Three layers. The arrows follow a measurement left to right, but the dependencies run the other way — and only ever one way.
At the bottom, four HAL modules wrapping the hardware: ADC, CAN, NVM, and timer plus watchdog. Each one is an interface, not a register map.
In the middle, six application services, each owning exactly one responsibility and one piece of state. Measurement owns samples, values and channel status. Sensor Converter dispatches the fixed conversion per type. Configuration owns the four channel modes. CAN Protocol decodes commands and packs values. NVM owns the two-copy record. Diagnostics collects faults, counters and the reset reason.
On the right, execution: a cyclic scheduler that decides when work runs, and a state machine that decides whether it's allowed to run at all. Deliberately separate concerns.
The left column is context, not a layer — those are external actors. And the payoff is the third card: because every service talks to interfaces, I can replace all four HAL modules with fakes and run the entire upper stack on a host PC.

## Slide 5
04 · DATA PATH
From timer tick to CAN frame
One pipeline serves all four channels. The configured sensor type selects the interpretation, not a separate code path.
Timer tick
start of a cycle
Read the ADC
one blocking scan,
all four channels
Which type?
look up the setting
Convert + check
raw count → value
Publish on CAN
value + status
THE CHANNEL SETTING DECIDES THE CONVERSION
TEMPERATURE
raw → input voltage →
temperature, by lookup
CURRENT
raw → input voltage →
amps, by fixed shunt model
VOLTAGE
raw → input voltage →
volts, by fixed divider ratio
DISABLED
no conversion runs;
status only, never a value
If a value is out of range
Mark that channel invalid and report it. Never publish a wrong number as though it were good.
WORKED EXAMPLE — CH2 CONFIGURED AS CURRENT
Shunt + amp
0.84 V at the pin
ADC
raw count 1042
Sensor Converter
fixed gain applied
18.5 A
status OK
CAN frame
value + status
Disabled is a channel state, not a fourth conversion — a disabled channel publishes its status and no value at all.
Notes: [1:10]
The measurement path. A timer tick starts a cycle, the ADC is read in one blocking scan of all four channels, then for each channel we look up its configured type, convert, range-check, and publish the value with its status.
One pipeline serves all four channels — the configured type selects the interpretation, not a separate code path. That matters for change: adding a fifth sensor type means one new conversion function and one new enum value. It touches nothing in the scheduler, nothing in the protocol layer, nothing in the acquisition code.
Two details. If a value is out of range we mark that channel invalid and report it — we never publish a wrong number as though it were good. And Disabled is a channel state, not a fourth conversion; a disabled channel publishes its status and no value at all.
The strip at the bottom walks one real reading through: 0.84 volts at the pin, raw count 1042, fixed gain applied, 18.5 amps out on CAN with status OK.

## Slide 6
05 · CONFIGURATION
Changing a channel type, safely
The acknowledgement is sent only after the new record is committed to non-volatile memory.
Fuel-cell
controller
CAN Protocol
Manager
Configuration
Manager
NVM
Manager
Measurement
Manager
SET_CHANNEL_TYPE (ch, type)
decoded, validated against the protocol
write the spare record copy
read back · CRC verified
move the commit marker + sequence
next scan uses the new type
result: accepted
ACK + channel status
step 1 ends here — the rest runs in step 4
THE CONFIGURATION RECORD — TWO COPIES
magic · version
sequence · CH0–CH3
CRC · commit
Invalid command
Rejected on arrival. A fault is reported and the active configuration is never touched.
NVM write or verify fails
The previously committed copy stays active. A diagnostic is raised and a NACK is returned.
The controller is never told a change succeeded unless the module could still honour it after an immediate reset.
Notes: [1:20]
Persistence is where designs like this usually go wrong, so it gets two slides. This is the write path.
The controller sends a set-channel-type command. The CAN Protocol Manager decodes and validates it. The Configuration Manager asks the NVM Manager to write the spare record copy — the spare, not the active one. That copy is read back and its CRC verified. Only then does the commit marker move. The next scan picks up the new type, and the result travels back out as an acknowledgement.
The one ordering decision that makes this power-fail safe: write and verify the spare first, move the marker last. Lose power before the marker moves and the committed copy is untouched.
Two failure branches. An invalid command is rejected on arrival and the active configuration is never touched. If the NVM write or verify fails, the committed copy stays active, we raise a diagnostic and return a NACK.
And the guarantee at the bottom: the controller is never told a change succeeded unless the module could still honour it after an immediate reset.

## Slide 7
06 · START-UP
What happens after a power interruption
The boot path decides which configuration is in force; the state machine decides what the module is allowed to do with it.
Power on
Read the NVM
both stored copies
Newest committed copy?
magic · sequence · CRC · commit
yes
Use the stored configuration
the module carries on as before
no
Use safe defaults
every channel disabled, and report it
Two copies are kept. A new record is written to the spare copy and verified before the commit marker moves, so an interrupted write always leaves the previous good copy intact — and if neither copy verifies, the module starts safe rather than guessing.
MODULE STATES
INIT
Entered on every reset. Loads and verifies the stored record. Nothing is sampled and nothing is published from this state.
RUN
The normal cycle: acquire, convert, publish, commit. Every enabled channel reports a value and a status.
DEGRADED
A channel, a conversion or the NVM has failed. Healthy channels keep publishing; faulty ones publish status only.
BUS-OFF RECOVERY
CAN bus-off was detected. Acquisition continues and transmission is retried under the protocol's recovery rules.
No state can publish a value without a status, so an unavailable reading is always visible to the controller as unavailable — never as a plausible zero.
Notes: [1:10]
The other half — the read path.
On power-on we read both stored copies, pick the newest one that is both valid and committed — magic number, sequence, CRC and commit marker — and use it. If neither verifies, we fall back to safe defaults with every channel disabled, and we report that we did. We don't guess.
Below that is the state machine I named on the architecture slide. INIT loads and verifies the record — nothing is sampled and nothing is published from INIT. RUN is the normal cycle. DEGRADED is where a channel, a conversion or the NVM has failed: healthy channels keep publishing, faulty ones publish status only, so one bad channel doesn't take the module down. BUS-OFF RECOVERY handles CAN bus-off — acquisition carries on while transmission retries under the protocol's recovery rules.
The rule across all four: no state can publish a value without a status, so an unavailable reading is always visible as unavailable, never as a plausible zero.

## Slide 8
07 · EXECUTION MODEL
A deterministic main loop
The same five jobs, in the same order, on every pass. No operating system, no dynamic allocation, no unbounded wait.
THE LOOP
Check CAN in
validate and stage a command
Read + convert
all four channels, by type
Publish values
value and status, on CAN
Commit if staged
only when a setting moved
Feed the watchdog
only on a clean pass
repeat, for ever
IN PSEUDOCODE
init_hardware();
config = load_committed_or_safe_defaults();
forever
{
if (can_command_pending()) stage_command();
if (time_to_measure()) read_and_convert_channels();
if (time_to_publish()) publish_values_and_status();
if (pending) commit_staged_config();
if (pass_completed_cleanly()) service_watchdog();
}
Why step 1 stages instead of writing
A flash page erase takes milliseconds. Writing it inside the command handler would make step 1 unbounded and quietly break the bounded-execution requirement. Step 1 validates and stages in RAM; step 5 writes, then acknowledges.
No unbounded waits
Every HAL wait has a timeout. The ADC scan is tens of microseconds, and the flash write has its own loop step.
The order is deliberate
Staged early, committed late — a new type is in force from the pass after it is acknowledged.
The watchdog is fed last
Only a pass that completed every step cleanly feeds it; an overrun becomes a logged reset.
Notes: [1:15]
The execution model is a cyclic executive — the same five jobs, in the same order, every pass. Validate and stage any CAN command, read and convert all four channels, publish, commit if a change is staged, and feed the watchdog. No operating system, no dynamic allocation, no unbounded wait.
The order is deliberate: commands are staged early and committed late, so a new channel type is in force from the pass after it is acknowledged.
No step waits without a bound — every HAL wait carries a timeout, so a dead peripheral is a reported fault, not a hang. And that's the orange card. An earlier version wrote flash inside the command handler. A page erase is milliseconds, which would have made that step unbounded and broken the determinism requirement two slides earlier. So step one stages in RAM; step five writes, then acknowledges.
And the watchdog is fed last, only on a pass that completed every step cleanly — so a job that overruns becomes a reset with a recorded reason, rather than a silent hang.

## Slide 9
08 · EXECUTION MODEL
The two routines that carry the requirements
Acquisition on the left, configuration change on the right. Both fail closed.
READING THE CHANNELS — EVERY PASS
read_and_convert_channels()
{
raw = adc_read_all();
for each channel ch
{
type = config.type[ch];
if (type == DISABLED)
{
status[ch] = DISABLED; /* never stale */
continue;
}
value[ch] = convert(raw[ch], type);
status[ch] = check_range(value[ch], type);
}
}
CHANGING A SETTING — STAGE, THEN COMMIT
stage_command(cmd)
{
if (!valid(cmd))
{ send_nack(cmd, INVALID); return; }
staged = config; /* whole record */
staged.type[cmd.ch] = cmd.type;
pending = true; /* RAM only */
}
commit_staged_config()
{
write_spare_copy(staged);
if (!read_back_and_crc_ok())
{ report_fault(NVM_WRITE); send_nack(staged, NVM);
pending = false; return; /* old copy stays */
}
move_commit_marker();
config = staged; /* flash, then RAM */
pending = false; /* else we re-commit */
send_ack(staged); /* last, on purpose */
}
Both routines fail closed: every early return leaves the previously committed configuration in force, a disabled channel publishes its status rather than a stale value, and send_ack is the last statement — so an accepted change is always a durable one.
Notes: [0:55]
Two routines carry most of the requirements.
On the left, reading the channels. One ADC scan, then per channel: look up the type, and if it's disabled, set the status to DISABLED and move on. That one line matters — without it, a channel you switch off keeps reporting its last status, which is exactly the stale-data bug the design is meant to prevent. Otherwise, convert and range-check.
On the right, the stage-then-commit pair. Staging validates and touches RAM only. Committing writes the spare copy, verifies it, and on any failure reports a fault, NACKs and discards — leaving the committed copy active. send_ack is the very last statement, after the marker has moved.
Both routines fail closed: every early return leaves the previously committed configuration in force. And both are ordinary C, testable on a host.

## Slide 10
09 · VERIFICATION
Most of it is proven without hardware
Each level tests only what the level below it could not.
ON A HOST PC — NO HARDWARE NEEDED
Unit tests
conversion boundaries · enum
validation · CRC · tick wrap-around
Component tests
mock ADC / CAN / NVM · protocol
encode and decode · every error path
ON THE REAL MODULE
Integration tests
configure → commit → reset →
measure → publish, on the target
Hardware in the loop
real analogue signals · a live CAN
network · real power interruption
FAULTS WE INJECT ON PURPOSE
a value leaves its valid range
→ channel marked invalid, no value published
an unknown or malformed command
→ rejected; the previous setting stays in force
power is cut mid-commit
→ the previously committed copy is still active
both stored copies fail their CRC
→ safe defaults, and the fault is reported
the CAN bus goes bus-off
→ acquisition continues; transmission recovers
a loop job overruns
→ watchdog reset, with the reason recorded
Every fault response written into the architecture is a test case — if the design claims a behaviour, something exercises it.
Notes: [1:00]
Verification. The shape of this slide is the argument.
Conversions, enum validation, CRC, protocol encode and decode, scheduler behaviour and every fault path are all testable on a host PC with mock drivers — which means they're testable on day one, before any board exists. Only integration and hardware-in-the-loop need the real module: real analogue signals, a live CAN network, a real power interruption.
Below that are the faults we inject deliberately. Value out of range, unknown command, power cut mid-commit, both copies failing CRC, bus-off, and a job overrunning. Each maps to a response the architecture already claims.
That's the discipline: if the design claims a behaviour, something exercises it. A fault response that exists only in a slide isn't a fault response.

## Slide 11
10 · CONCLUSION
What the design guarantees — and what it does not
WHAT THE DESIGN GUARANTEES
One pipeline
Four channels, one scan. The configured type chooses the meaning, not the code path.
One owner per state
No service writes another service's data.
Interfaces, not registers
IAdc / ICan / INvm / ITimer, so every service runs on a host with mocks.
Committed, not written
CRC, a sequence number and a commit marker survive a power cut.
Faults stay visible
A reading is never published without its status.
OPEN QUESTIONS FOR THE SYSTEM OWNER
· Exact CAN identifiers, cycle times and command/response layout.
· Required accuracy and update rate for each sensor type.
· Does the chosen MCU and front end support open / short detection?
· Expected configuration writes over life — this sizes NVM wear handling.
· Must the module accept a firmware update over CAN?
· May a channel change type while the system is running?
Honest limits
Cycle times in this deck are illustrative — the real periods come from the system requirements. The flash programming detail follows the chosen microcontroller's data sheet, and open / short diagnostics are claimed only where the silicon actually supports them.
Notes: [0:55]
To close.
What it guarantees: one pipeline for four channels; one owner per piece of state; interfaces rather than registers, so everything runs on a host with mocks; configuration committed rather than merely written; and faults that stay visible.
What I'd need from the system owner before writing production code: the exact CAN identifiers and cycle times, the required accuracy per sensor type, whether the chosen part supports open and short detection, the expected configuration writes over life — that sizes NVM wear handling — whether firmware update over CAN is in scope, and whether a channel may change type while the system is running.
And the honest limits: the cycle times here are illustrative, the flash programming detail follows the chosen microcontroller's data sheet, and I've claimed open-short diagnostics only where the silicon supports them.
Happy to go deeper on any of it.